## Slide 1: Machine Learning Overview
Edward Wang, Ph.D.

## Slide 2: Data Analytics for Manufacturing
What happened?
Why exactly?
What will happen?
What is the plan?
Descriptive
Historical analysis to establish statistical benchmarks for updating knowledge base
Statistical measures Regression Correlation analysis Principal component analysis Visualization
Diagnostic
Identification of root causes and key factors to facilitate decision making
Time-frequency analysis Bayesian inference K-means clustering Support vector machine Neural network
Prognostic
Discovery and analysis of system variation pattern & quantification of uncertainties
Decision trees Wiener process Support vector regression Neural network Kalman filter Particle filter
Prescriptive
Action scheduling and process optimization for improved KPIs
Sensitivity analysis Reliability analysis Local and global optimization Linear and nonlinear programing

## Slide 3: Classification of Process Monitoring Issues
Dresser
Conditioning motion
Abrasive type
Abrasive density
Abrasive configuration
Slurry
Type
Abrasive size
pH Value
Abrasive hardness
Concentration
Flow rate
Additive
Zeta potential
Others
Temperature
Polishing time
Wafer
Pressure
Pattern hardness
Film type
Wafer size
Pad
Hardness
Compressibility
Relative speed
Worn degree
MRR [nm/min]

## Slide 4: Classification of Process Monitoring Issues
Axis Drive
Current/power
Velocity
Position
Ball Screw
Force
Dynamometer
Cutting force
Spindle Motor
Current/power
Speed
Position
Force/Torque
Machine Structure
Vibration
AE
Cutting Process
AE
Vibration
Online Measurement
Offline Measurement
Microscope
  From sensing data to system performance
  From sensing data variation pattern to system performance degradation pattern

## Slide 5: Classification of Process Monitoring Issues
Operation Condition | Rotational speed: 1,800 RPM
Measurement | Four sensors Sampling frequency: 8192 Hz
Artificially made 4 fault severity levels
Level #1
Level #1
#2
#3
#4
Broken gear
Large crack
Small
crack
Normal

## Slide 6: Machine Learning Techniques
Machine Learning
Unsupervised Learning
Supervised Learning
Clustering
Dimensionality Reduction
Regression
Classification
Hierarchical?
Probabilistic?
Yes
No
Yes
No
Topic model?
Probabilistic?
Yes
No
Yes
No
Speed
Accuracy
Linear regression
Logistic regression
Thin plate Spline
Decision tree
Naive Bayes
Linear SVM
Random forest
Neural network (Deep Learning)
Kernel SVM
Gradient boosting tree
Hierarchical clustering
Gaussian mixture model
K-means
Principal component analysis
Singular value decomposition
Latent dirichlet allocation
Discover the relationship between inputs to human-labeled outputs
Learn similarities and differences among data

## Slide 7: Machine Learning Techniques: Comparison
Technique | Expression | Accuracy | Speed | Automatic feature learning | Performance on small dataset | Handling with non-linearity | Parameter to be tuned
Linear regression |  | Low | Fast | No | Good | Poor | None
Logistic regression |  | Low | Fast | No | Good | Poor | None
Naive Bayes |  | Low | Fast | No | Good | Poor | Some
Linear SVM |  | Low | Fast | Yes | Good | Poor | Some
Thin plate splines |  | High | Fast | No | Good | Good | Some
Kernel SVM |  | High | Slow | Yes | Good | Good | Some
Random forest |  | High | Slow | Yes | Poor | Good | Some
Boosting tree |  | High | Slow | Yes | Poor | Good | Some
Neural Network |  | High | Slow | Yes | poor | Good | Many
B: number of trees
Supervised ML: Discover the relationship between system inputs (e.g. process parameters) and outputs (e.g. part quality)

## Slide 8: Questions to Answer Before Building a ML Model
What question(s) am I trying to answer? Do I think the data collected can answer that question?
What is the best way to phrase my question(s) as a machine learning problem?
Have I collected enough data to represent the problem I want to solve?
What features of the data did I extract, and will these enable the right predictions?
How will I measure success in my application?
How will the machine learning solution interact with other parts of my research or business product?